SPARLITE 90LI							SPAR, INC.

Material Safety Data Sheet						U.S. Department of Labor

May be used to comply with						Occupational Safety and Health Administration

OSHA'S Hazard Communication Standard.					(Non-Mandatory Form)

29 CFR 1910.1200. Standard must be					Form Approved OMB No. 1218-0072

consulted for specific requirements

| IDENTITY (As Used on label and list) SPARLITE 90LI | Note: Blank spaces are not permitted. If any item is not applicable or no information is available, the space must be marked to indicate that. |
| --- | --- |

# SECTION I

| Manufacture's Name: SPAR, INC | Emergency Telephone Number: 256-435-9342 |
| --- | --- |
| Address (Number, Street, City, State and Zip Code P.O. Box 909 | Telephone Number for information: 256-435-9342 |
| 917 Francis Street | Date Prepared: September 23, 2004 |
| Jacksonville, Alabama 36265 | Signature of Preparer(optional) |

SECTION II - Hazardous Ingredients/Identity Information:

| Hazardous Components | Cas No. | % | ACGIH TLV | LD50 | LC50 |
| --- | --- | --- | --- | --- | --- |
| Crystalline Silica (Total) | N/A | < 20 | N/A | N/A | N/A |
| Above includes:Quartz | 14808-60-7 |  | 0.1 mg/m3 | N/A | N/A |
| Cristobalite | 14464-46-1 |  | 0.05 mg/m3 | N/A | N/A |
| Tridymite | 15468-32-3 |  | 0.05 mg/m3 | N/A | N/A |
| Calcium Aluminate Cement | 12042-68-1 | < 50 | 10 mg/m3 | N/A | N/A |

Threshold Limit Value for respirable dust containing crystalline silica:

OSHA PEL:  10 divided by (% Quartz + 2(% Tridymite + Crystobalite) in terms of mg/m3

CALIFORNIA RESIDENTS:  This product contains one or more chemicals known to the state of California to cause cancer, birth defects or other reproductive harm.

SECTION III- Physical/Chemical Characteristics:

| Boiling Point | N/A | Specific Gravity (g/cc) | 1.4 |
| --- | --- | --- | --- |
| Vapor Pressure (mm Hg.) | N/A | Melting Point | N/A |
| Vapor Density (AIR-1) | N/A | Evaporation Rate (Butyl Acetate- 1) | N/A |

Solubility in Water: VERY LOW

Appearance and Odor:  DRY SANDY TO POWDER - NO ODOR

Section IV - Fire and Explosion Hazard Data:

| Flash Point (Method Used) N/A | Flammable Limits N/A | LEL N/A | UEL N/A |
| --- | --- | --- | --- |

Extinguishing Media:  IGNITION UNLIKELY - ANY MEDIA

Special Fire Fighting Procedures: N/A

Unusual Fire and Explosion Hazards:  N/A

PAGE 1			OSHA 174, 9-1986

# SPARLITE 90LI

# Section V - Reactivity Data

| Stability | Unstable |  | Conditions to Avoid |
| --- | --- | --- | --- |
|  | Stable | X |  |

Incompatibility: (Materials to Avoid)   N/A

Hazardous Decomposition or Byproducts:  N/A

| Hazardous Polymerization | May Occur |  | Conditions to Avoid |
| --- | --- | --- | --- |
|  | Will Not Occur | X |  |

Section VI - Health Hazard Data:

Route(s) of Entry:		Inhalation? DUST			Skin?			           Ingestion? DUST

Health Hazard:  (Acute and Chronic)  SEE BELOW

Carcinogenicity:		NTP?				IARC Monographs?		OSHA Regulated?

NO				YES				NO

Signs and Symptoms of Exposure:	Chronic overexposure to dust containing respirable sized crystalline silica can cause delayed lung injury

(silicosis).  Inhalation of dust containing crystalline silica may contribute to pre-existing pulmonary

diseases such as asthma and lung disorders associated with smoking.  IARC studies have shown sufficient

evidence from animal studies to categorize crystalline silica as a group 1 carcinogen.

Medical Conditions

Generally Aggravated by Exposure:	Any pre-existing lung disorder.

Emergency and First Aid Procedures :  IN CASE OF EYE CONTACT, IMMEDIATELY FLUSH REPEATEDLY WITH WATER.

CONSULT A PHYSICIAN IF IRRITATION PERSISTS.

Section VII - Precautions for Safe Handling and Use:

Steps to be taken in Case Material is Released or Spilled: CLEAN UP WITH BROOM AND/OR SHOVEL.  AVOID BREATHING 						             NUISANCE DUST.

Waste Disposal Method:  APPROVED LANDFILL.

Precautions to be Taken in Handling and Storing:  STORE IN DRY LOCATION.

Other Precautions:   N/A

Section VIII - Control Measures:

Respiratory Protection: (Specify Type) NIOSH APPROVED DUST RESPIRATOR IF WORKING IN DUST CONDITIONS.

| Ventilation | Local Exhaust TO CONTROL DUST | Special N/A |
| --- | --- | --- |
|  | Mechanical (General) N/A | Other N/A |

| Protective Gloves: REGULAR GLOVES | Eye Protection: SAFETY GLASSES |
| --- | --- |

Other Protective Clothing or Equipment:  N/A

Work/Hygienic Practices:   N/A

PAGE 2		*U.S.G.P.O: 1966-491-529/45775