SPAR, INC.

P.O. BOX 909

JACKSONVILLE, ALABAMA 36265

EMERGENCY TELEPHONE NO. 256-435-9342

DATE ISSUED: MAY 20, 1987         DATE REVISED: JANUARY 15, 1997

MATERIAL SAFETY DATA SHEET

*******************************************************************************************************************

SPAR, INC. PRODUCT NAME:	SPARGRAPH 85 SCR

------------------------------------------------------------------------------------------------

SECTION I-PRODUCT IDENTIFICATION

TRADE NAME: Refractory ram or plastic

SYNONYM OR GENERIC ID:	Refractory plastic material

--------------------------------------------------------------------------------------------------SECTION II-HAZARDOUS COMPONENTS

INGREDIENT	PERCENT	CAS NO.	TLV-TWA

CALCINED BAUXITE		40-60	1318-16-7	10 mg/m3**

ALUMINUM OXIDE     		 5-30	1344-28-1	10 mg/m3**      	SILICON CARBIDE		10-20	409-21-2	10 mg/m3 		RAW Al2O3-SiO2		 0-10	1302-76-7	5 mg/m3

ALUMINUM SILICATE	  	 5-15	1332-58-7	10 mg/m3***

GRAPHITE		 5-15	7782-42-5	2.5 mg/m3***

COAL TAR PITCH     		1-5	65996-93-2	0.2 mg/m3

**  TOTAL DUST                         *** RESPIRABLE DUST

None of the ingredients are subject to reporting under SARA Section 313.

-----------------------------------------------------------------------------------------------

SECTION III-PHYSICAL DATA

BOILING POINT(0F): N/A 	SPECIFIC GRAVITY(H20=l): 1.5-2.0
	VAPOR PRESSURE(mmHg):N/A	PERCENT VOLATILES by VOLUME(%): N/A
		EVAPORATION RATE: N/A
	SOLUBILITY IN WATER: Insoluble

APPEARANCE AND ODOR: Black granular wet mix with no distinct odor

------------------------------------------------------------------------------------------------

# SECTION IV-FIRE AND EXPLOSION DATA

FLASH POINT (METHOD USED):	None

FLAMMABLE LIMITS:	None

EXTINGUISHING MEDIA:	As required for surrounding media.

SPECIAL FIREFIGHTING PROCEDURES:	Will not burn, as appropriate for surrounding fire.

UNUSUAL FIRE & EXPLOSION HAZARDS:	Avoid the generation of entrapped steam during dryout to prevent explosive spalling. Use proper curing and dryout procedures.

------------------------------------------------------------------------------------------------

SECTION V-HEALTH HAZARD DATA

THRESHOLD LIMIT VALUE:	Not determined for product. See Section II above for components.

EFFECTS OF ACUTE OVEREXPOSURE:The polymer contains polycyclic aromatic hydrocarbons. Certain polycyclic aromatics have been shown to cause skin cancer in experimental animals following prolonged and/or repeated contact and occur in humans in the absence of good personal hygiene practices. Overexposure to graphite dust may result in irritation to the respiratory tract, skin, and eyes. Long term inhalation of graphite dust may cause delayed lung damage. Persons with existing respiratory diseases or previous exposure may be at a greater risk of developing adverse health effects when handling this product

PRIMARY ROUTE(S) OF ENTRY:	Inhalation, skin contact

Crystalline Silica (Quartz) is listed as a carcinogen to humans by IARC

(Classification 1) and by OSHA. Long term inhalation of silica dust may cause delayed lung damage (Silicosis).

PAGE 1

SPAR, INC.

MATERIAL SAFETY DATA SHEET

(CONTINUED-SPARGRAPH 85 SCR)

FIRST AID:

IF ON SKIN:	Wash with soap and water or waterless hand cleaner.

IF IN EYES:	Flush eyes immediately with plenty of water for at least 15 minutes.

Call a physician.

IF INGESTED:		Induce vomiting and get medical attention.

IF INHALED:	Remove to fresh air. If not breathing, give artificial respiration. If breathing is difficult, give oxygen and call a physician.

------------------------------------------------------------------------------------------------SECTION VI-REACTIVITY DATA

HAZARDOUS POLYMERIZATION:	Will not occur

STABILITY:	STABLE

INCOMPATIBILITY:	N.A.

HAZARDOUS DECOMPOSITION PRODUCTS:	CO, CO2 when heated.

CONDITIONS TO AVOID:	N.A.

------------------------------------------------------------------------------------------------SECTION VII-SPILL OR LEAK PROCEDURES

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED:

Shovel into containers and avoid the generation of respirable dust.           WASTE DISPOSAL METHOD: Industrial solid waste landfill in accordance with local,

state, and federal laws.

------------------------------------------------------------------------------------------------SECTION VIII-PROTECTIVE EQUIPMENT

RESPIRATORY:	Use NIOSH/MSHA approved respirator.

VENTILLATION:	Use local exhaust to remove dust and fumes.

PROTECTIVE GLOVES:	Non-porous type.

EYE PROTECTION:	Safety glasses, goggles, or faceshield if work area is dusty, and to prevent eye contact when applying product.

OTHER:	N.A.

------------------------------------------------------------------------------------------------

SECTION IX-SPECIAL PRECAUTIONS OR OTHER COMMENTS

PRECAUTIONS TO BE TAKEN IN HANDLING AND STORAGE:

Store in cool, dry environment. Protect from freezing.

OTHER PRECAUTIONS:	Avoid the inhalation of respirable dust during refractory tearout due to the possible presence of Crystalline Silica and/or other hazardous substances.

------------------------------------------------------------------------------------------------

The information accumulated herein is believed to be accurate but is not warranted to be accurate whether originating with SPAR,INC. or not. This data relates to the specific product designated herein and does not relate to use in combination with any other material or in any process. Since conditions of use are beyond our control, any warranties, expressed or implied, in connection with any use of this information or the product are disclaimed. Nothing is intended to be a recommendation or license to operate or infringe valid patents. Recipients are advised to confirm in advance of need that the information is current, applicable, and suitable to their circumstances.

PAGE 2